## Slide 1: National Oil and Hazardous Substances Pollution Contingency Plan
Monitoring Requirements for Use of Dispersants and Other Chemicals
Subpart J Final Monitoring Rule 300.913
Docket ID Number: EPA–HQ–OPA–2006–0090
Published in the Federal Register July 27, 2021, with the effective date of January 24, 2022
Notes: Published in the Federal Register July 27, 2021, with the effective date of January 24, 2022
Can be found on regulations.gov under docket ID number EPA-HQ-OPA-2006-0090

## Slide 2: Background on Final Monitoring Rule
April 2010 Deepwater Horizon underwater well blowout
  ~ 1 Million Gallons of dispersants deployed over a 3-month period on surface slicks over thousands of square miles
  ~ Three quarters of a million gallons injected directly into the oil gushing from the well riser for the first time
  This raised questions about the challenges of making dispersant use decisions in response operations for certain atypical dispersant use situations
    Such A-Typical use was neither envisioned or addressed in current RRT dispersant use plans and the SMART monitoring program
  EPA established new monitoring requirements under Subpart J of the NCP to address these challenges.

## Slide 3: Monitoring the Use of Dispersants
Monitoring rule requirements for certain discharge (atypical) situations in this action supplements the existing regulatory provisions under Subpart J
    Subpart J already includes test data and information requirements for chemical agents on the product schedule
    As well as procedures for authorizing the use of chemical agents to respond to oil discharges and threats of discharges
The New Monitoring Rule (300.913) establishes requirements for the responsible party to:
  Monitor subsurface use of dispersants
  Monitor surface use of dispersants on oil discharge of 100,000 gallons occuring within 24hrs
  Monitor surface use of dispersants on an oil discharge for more than 96 hours
  Submit a Dispersant Monitoring Quality Assurance Project Plan (DMQAPP) to the OSC
Intended to address the challenges of atypical dispersant use situations
Notes: Under the NCP 40 CFR 300.120 the OSC coordinates, directs, and reviews the work of the Responsible Party
This approach is consistent with the NCP response framework, taking advantage of the knowledge and geographic proximity of the responsible party as applicable, and allowing for the effective allocation of limited governmental resources.
Does not preclude the OSC from seeking a qualified third party to conduct additional monitoring or testing, from requiring the responsible party to use a third party to conduct the monitoring or testing where the osc deems it appropriate, or from seeking supplemental data and information separately.
Does not preclude the consideration of third-party testing or test results.
Does not amend any regulatory requirements or authorities

## Slide 4: Monitoring the Use of Dispersants cont.
The requirements are established for the responsible party as they operate in those environments where applicable discharges may occur and should be in the best position to monitor the response
DMQAPP is not intended to establish a DMQAPP approval timeline for the OSC relative to dispersant use.
DMQAPP submission is intended to provide the OSC, and other agencies with NCP responsibilities, with a better understanding of the monitoring data to inform dispersant use decisions
The OSC may request response supporting agencies provide feedback on the submitted DMQAPP and has the discretionary authority to require the responsible party to address any concerns associated with it.
Responsible party is required to implement the new monitoring requirements when these dispersant use conditions are met, and for the duration of dispersant use
Notes: DMQAPP: Dispersant Monitoring Quality Assurance Project Plan
Dispersant operations will not be held up while a DMQAAP is being drafted

## Slide 5: Final Monitoring Rule
Monitoring and data submissions that serve a basis for this rule were established in the 2013 NRT Environmental Monitoring for Atypical Dispersant Operations document
Industry and OSROs have been preparing to monitor dispersant use since the issuance of the 2013 guidance document
Notes: Document recommends establishing a Dispersant Environmental Monitoring Unit within the Environmental Unit to coordinate and oversee the implementation of the sampling and monitoring activities and, as appropriate, any additional sampling and monitoring activities required by circumstances of the particular response.
The SSC directly coordinates with the DEMU to ensure an unfiltered data flow to the OSC and government decision-makers, including the EPA representative and the federal Natural Resources Trustees

## Slide 6: Monitoring Elements
The monitoring elements in the final rule cover several key areas
  Source characteristics and information on dispersant application
  Water column sampling
  Oil distribution analysis
  Ecological characterization
  Immediate and daily reporting
Notes: The purpose of dispersant use monitoring is to gather data and information on dispersant application to understand dispersed oil behavior
  including transport by water currents and plume characteristics,
  and to identify and assess the potential adverse environmental effects resulting from dispersant use.

## Slide 7: Information on Dispersant Application
The new monitoring regulation requires the Responsible Party to document
  The characteristics of the source oil
  The best estimate of the oil discharge volume or flow rate
    Periodically reevaluated as conditions dictate
    Include description of method, associated uncertainties, and materials
  The dispersant used
    Rational for dispersant choice(s)
    Results of any efficacy and toxicity tests specific to area or site conditions
    Recommended dispersant-to-oil ratio
  The application method(s) and procedures
    Description of the equipment to be used
    Hourly application rates, capacity, and total amount of dispersant

## Slide 8: Water Column Sampling
  Collect ambient background, baseline, and dispersed oil plume water column samples following standard operating and quality assurance procedures
    Ambient background water column samples from areas not affected by the discharge of oil:
      At closest safe distance from discharge, as determined by OSC
      In all directions of likely oil transport
      Considering surface and subsurface currents
    Baseline water column samples absent dispersant application
      At such depths and locations affected by the oil discharge
      Considering surface and subsurface currents, oil properties, and other relevant discharge conditions
    Dispersed oil plume water column samples
      At such depths and locations, where dispersed oil is likely to be present
      Considering surface and subsurface currents, oil properties, and other relevant discharge conditions
Notes: The agency is not requiring the use of specific oil size droplet measurement methods or instrumentation
The agency is not requiring the use of single instrument, methodology, vessel, or ROV be used to collect the required information
How to collect the information is left for the RP to determine and document in the DMQAPP

## Slide 9: Water Column Sampling
  Analyze for:
    In-situ oil droplet size distribution
      Including mass or volume mean diameter for droplet sizes ranging from 2.5 to 2,000 µm, with the majority of data collected between the 2.5 and 100 µm size
    In-situ fluorometry/fluorescence
      targeted to the type of oil discharged and referenced against the source oil
    Total petroleum hydrocarbons and the individual resolvable constituents
      volatile organic compounds (VOC)
      Aliphatic hydrocarbons
      monocyclic, polycyclic, and other aromatic hydrocarbons including
        alkylated homologs, and hopane and sterane biomarker compounds
    Dissolved Oxygen (DO) (subsurface only)
    Methane, if present (subsurface only)
    Heavy metals, including nickel and vanadium
    Turbidity, water temperature, pH, and conductivity
Notes: Oil droplet size distribution is an indicator of dispersant effectiveness and can be used to inform plume modeling.
Relative significant changes in the fluorometric output indicates the possible presence of a dispersed plume.
DO is an indicator of potential injury in the subsea ecological system. An increase in organic carbon loading enhances microbial activity, thereby increasing respiration and depleting oxygen.
Understanding methane concentrations can inform the key indicator factor for dissolved oxygen since biodegradation of methane may contribute to oxygen depression
Conduct oil analysis to determine the effects of the dispersed oil plume on aquatic life. Will the dispersed oil persist in the water column, and will it come into contact with the benthos community?
  Compare water sample data to ecological toxicity benchmarks for aquatic organisms to assess potential toxicity risks

## Slide 10: Oil Distribution Analyses and Ecological Characterization
Characterize dispersant effectiveness and oil distribution
  Considering available technologies
  Considering condition of oil, dispersant, and dispersed oil components from the discharge location
  Describe associated uncertainties
Characterize ecological receptors/habitats that may be present in the discharge area and their exposure pathways
  Include species in sensitive life stages, transient or migratory species, breeding or breeding-related activities, and threatened and/or endangered species potentially exposed to undispersed oil, dispersed oil, and dispersant alone
  Estimate an acute toxicity level of concern for the dispersed oil using available dose-response information relevant to potentially exposed species

## Slide 11: Immediate and Daily Reporting
Immediate Reporting to the OSC and RRT
  Deviation of more than 10 percent from mean hourly subsurface dispersant use rate from authorized 24 hours volume and the reason for the deviation
  Ecological receptors of environmental importance, and any other ecological receptors as designated by the OSC or the Natural Resource Trustees, including any threatened or endangered species that may be exposed based on dispersed plume trajectory modeling and level of concern information
Daily Reporting to the OSC and RRT
  Water sampling and data analyses
  For each application platform, the actual amount of dispersant used for each one-hour period and the total amount of dispersant used for the previous 24-hour reporting period
  All collected data and analyses within timeframe necessary for operational decisions as authorized by the OSC (e.g., within 24 hours of collection), including documented observations, photographs, video, and any other information related to dispersant use, unless an alternate time frame is authorized by the OSC
  For analyses requiring more than 24 hours due to analytical methods, provide data and results as available but no later than five days, unless an alternate timeframe is authorized by the OSC
  Daily transport estimates, using available technology as described in § 300.913(c), of dispersed and non-dispersed oil, associated volatile petroleum hydrocarbons, and dispersants

## Slide 12: Final Monitoring Rule Key Points
Final Monitoring Rule only applies to A-typical dispersant operations
  Subsurface dispersant application
  Surface use of dispersants on an oil discharge of 100,000 gallons occuring within 24hrs
  Surface use of dispersants on an oil discharge for more than 96 hours
Final Monitoring Rule does not inhibit the OSCs ability to authorize dispersant use prior to DMQAPP submittal by the RP
The Agency does not determine how water column sampling is to be conducted, that is left up to the RP to determine and document in the DMQAPP

## Slide 13: Thank You
William Martin
EPA Region 3 Representative to the National Subpart J Rule Writing workgroup