## Slide 1: The Hazard Communication Standard SDS Requirements Supporting Emergency Responders
Dalton L. Moore MS, CSP OSHA Directorate of Enforcement Programs Office of Health Enforcement

## Slide 2: OSHA’s HCS 2024 Update
The 2024 update to the Hazard Communication Standard (HCS) aims to enhance worker protection by improving the dissemination and clarity of information regarding chemical hazards.
This directly supports emergency responders, especially during incidents like oil spills and hazardous material releases.
The HCS update aligns with the Globally Harmonized System of Classification and Labeling of Chemicals (GHS), primarily Revision 7, bringing a more consistent and coherent approach to hazard communication.

## Slide 3: Key Dates (Implementation Dates for HCS 2024)
The final rule updating and revising the HCS was published on May 20, 2024 (89 FR 44144), and became effective on July 19, 2024. The document extending the compliance dates became effective on January 15, 2026
Manufacturers, importers, and distributors evaluating substances must comply with all modified provisions of the HCS no later than May 19, 2026
Employers must, as necessary, update alternative workplace labeling, update their hazard communication program, and provide additional employee training for newly identified physical, health, or other hazards related to substances no later than November 20, 2026
Chemical manufacturers, importers, and distributors evaluating mixtures must comply with all modified provisions of the HCS no later than November 19, 2027

## Slide 4: Cont.
Transition Period: Between May 20, 2024, and these extended compliance dates, chemical manufacturers, importers, distributors, and employers have the option to comply with either the previous version of the standard (77 FR 17574, March 26, 2012), the updated HCS (89 FR 44144, May 20, 2024), or both. Specifically, they may comply with either the current section or § 1910.1200 revised as of July 1, 2023, or both

## Slide 5: HCS 2024 Compliance Directive
OSHA Instruction, CPL 02-02-079, Inspection Procedures for the Hazard Communication Standard (HCS 2024)
Signed April 30, 2026
Effective May 19, 2026
Cancels the HCS 2012 Directive, archived here.

## Slide 6: Why HCS Matters for Emergency Responders
Goal: To ensure that information about the identities and hazards of chemicals is available and understandable to workers.
Impact on Emergency Responders: Improved and standardized hazard communication directly supports emergency responders by providing clearer and more structured information for safe and effective incident management.
The updated HCS clarifies existing requirements and incorporates new hazard classes and categories

## Slide 7: Key Changes in HCS 2024 Supporting Responders
The HCS 2024 update introduces several changes that enhance hazard communication for emergency responders:
Inclusion of New Hazard Classes and Categories:
  Incorporates "chemicals under pressure" and expands on "flammable gases" and "aerosols".
  The definition of "Physical hazard" now explicitly includes "chemicals under pressure".
  This ensures a more comprehensive hazard assessment and clearer understanding of potential risks.
Improved Communication for Bulk Shipments:
  Hazard information for chemicals in tank trucks or rail cars can be displayed on the vehicle or transmitted via shipping papers/bills of lading.
  If stored before offloading, HCS requirements apply, and they can be labeled as stationary process containers, critical for first responders in transit accidents or storage facility incidents.

## Slide 8: Key Changes in HCS 2024 Supporting Responders (cont.)
Alignment with Department of Transportation (DOT) Requirements:
  Aligns the standard with DOT labeling requirements, allowing labels to display both DOT and HCS pictograms for the same hazard.
  This consistent visual language simplifies hazard recognition for emergency personnel.
Addressing Combustible Dusts:
  The HCS update specifically defines and requires communication of combustible dust hazards.
  This helps responders anticipate explosion risks from finely divided solid particulates.
Definition of Foreseeable Emergency:
  The standard's definition of "foreseeable emergency" directly addresses scenarios relevant to spills and releases.
  Includes "equipment failure, rupture of containers, or failure of control equipment which could result in an uncontrolled release of a hazardous chemical into the workplace". This clarifies employer responsibility to communicate hazards for such events.

## Slide 9: Standardized Safety Data Sheet (SDS) Format
Mandatory 16-Section Format:
  The HCS 2024 mandates a specific 16-section format for SDSs.
Enhanced Accessibility:
  This standardization ensures that critical information is consistently located, making it easier and faster for emergency responders to find necessary details during urgent situations.
Explicit "No Information" Statement:
  If no relevant information is found for a subheading, the SDS must explicitly state "no applicable information was found".
Notes: Table above was from OSHSPA presentation from DEP, February 2026
The UEH initiative was piloted last year with the Heat NEP. The pilot turned resulted in 189 Heat NEP inspections with the UEH code, most all from the CHI Region (178) and the rest (11) from the DAL Region.
This year, continues with Heat NEP – CPL 03-00-024, and is
expanded to:
Crystalline Silica NEP – CPL 03-00-023
Fall Prevention/Protection NEP – CPL 03-00-025
Trenching and Excavation NEP – CPL 02-00-161

## Slide 10: Critical SDS Sections for Emergency Response
These sections provide immediate identification and hazard insights:
Section 1: Identification
  Includes the emergency phone number for the responsible party.
  This number should connect to a knowledgeable person able to provide additional information, potentially through a contracted service like Chemtrec.
Section 2: Hazard(s) Identification
  Provides the hazard classification (class and category), signal word, hazard statement(s), symbol(s) (pictograms without the border), and precautionary statement(s).
  Requires the listing of Hazards Not Otherwise Classified (HNOC) identified during classification, which is vital for comprehensive emergency planning.

## Slide 11: Critical SDS Sections for Emergency Response (cont.)
These sections guide initial response actions:
Section 4: First-aid measures
  Clearly outlines necessary first-aid measures based on routes of exposure (inhalation, skin, eye contact, ingestion).
  Describes the most important symptoms (acute and delayed).
  Indicates whether immediate medical attention or special treatment is needed, directly guiding initial medical response.
Section 5: Fire-fighting measures
  Specifies suitable and unsuitable extinguishing media.
  Identifies specific hazards arising from the combustion of the material.
  Details the required Personal Protective Equipment (PPE) and precautions for firefighters. This information is indispensable for safely tackling fires involving hazardous materials.

## Slide 12: Critical SDS Sections for Emergency Response (cont.)
These sections detail containment and protection strategies:
Section 6: Accidental release measures
  Provides critical instructions on personal precautions, protective equipment, and emergency procedures.
  Covers methods and materials for containment and cleaning up spills and releases. This section is directly relevant to managing oil spills and hazardous material releases.
Section 8: Exposure controls/personal protection
  Lists OSHA Permissible Exposure Limits (PEL), ACGIH Threshold Limit Values (TLV), and other recommended exposure limits.
  Describes appropriate engineering controls and individual protection measures, such as PPE, which aids responders in selecting the correct gear to protect themselves.

## Slide 13: Critical SDS Sections for Emergency Response (cont.)
These sections help prevent incident escalation and inform medical treatment:
Section 10: Stability and reactivity
  Details the chemical's reactivity, stability, and possibility of hazardous reactions.
  Lists conditions to avoid (e.g., static discharge, shock), incompatible materials, and hazardous decomposition products. This information is vital for preventing the escalation of an incident.
Section 11: Toxicological information
  Describes the various toxicological effects, likely routes of exposure, symptoms related to physical/chemical/toxicological characteristics.
  Covers delayed/immediate/chronic effects from short- and long-term exposure. This informs medical treatment and long-term health monitoring for exposed responders.
Notes: No OTI Webinar for CSHOs
Media:
Inside OSHA
EHS Leaders
Occupational Health & Safety
Safety+Health Magazine
Associated Builders and Contractors
Construction Dive
Woodworking Network
Cleaning & Maintenance Management
CleanLink
National Law Review
Bloomberg Law

## Slide 14: Key Takeaway: Integrations with HAZWOPER Training
The HCS training program is designed to integrate with the Hazardous Waste Operations and Emergency Response (HAZWOPER) standard (29 CFR 1910.120).
This means that training for emergency procedures, including those for spills and releases, can fulfill requirements for both standards.
This integration ensures responders are well-prepared for hazardous material incidents.

## Slide 15: Key Takeaway: Prepare for Combustible Dust Hazards
The HCS Update specifically defines and requires communication of combustible dust hazards, helping responders anticipate explosion risk that might not have been adequately communicated previously

## Slide 16: Key Takeaway: Alignment with department of Transportation requirements
HCS 2024 aligns with DOT labeling requirements, and OSHA intends to allow labels to display both DOT and HCS pictograms for the same hazard. This creates a consistent visual language, simplifying hazard recognition for emergency personnel. However, where DOT requires no pictograms (e.g., for carcinogens), HCS pictograms must appear

## Slide 17: Key Takeaway: Understand “Foreseeable Emergency”
The standard's definition of "foreseeable emergency" directly addresses scenarios relevant to spills and releases, including equipment failure, container rupture, or control equipment failure that could lead to an uncontrolled chemical release. This clarifies the employer's responsibility to communicate hazards for such events.

## Slide 18: Key Takeaway: Levearge Improved Communication for Bulk Shipments
For hazardous chemicals transported in tank trucks or rail cars that serve as their immediate containers, labeling information can be displayed on the vehicle or transmitted via shipping papers or bills of lading. If these vehicles are stored before offloading, HCS requirements apply, allowing them to be labeled as stationary process containers. This ensures hazard information is available throughout transportation and temporary storage phases, critical for first responders in transit accidents or storage facility incidents

## Slide 19: Conclusion
The HCS 2024 updates to SDS content and format, along with enhanced hazard classification and clearer definitions of emergency scenarios, significantly improve the quality and accessibility of information for emergency responders.
These changes enable responders to make more informed decisions and take appropriate actions during hazardous material releases and potential incidents like oil spills.

## Slide 20: Compliance Assistance Materials
Redline Strikeout
Hazard Classification Guidance
Frequently Asked Questions (FAQs)
As OSHA issues further compliance assistance materials, they will be located at OSHA’s HCS Page or the HCS Rulemaking Page.

## Slide 21: Questions:

## Slide 22: OSHA Contact Information
We want every worker to go home safe
osha.gov
800-321-OSHA (6742)